F.  Clyde’s  Cider  Mill

Established  1898

Old  Mystic,  Connecticut

National Mechanical Engineering Site Dedication October 29, 1994

The American Society of

Mechanical Engineers

History  of  Cider  in  the  U.S.

Apple cider dates back to the earliest days of

required equipment that was operated only once a

year, farmers found it more convenient to travel consid- erable distances to bring their fruit to a large mill for

| English settlement in the thirteen colonies. Colonists | processing into juice (sweet cider). Surplus apples could be sold or bartered to the mill owner who would |
| --- | --- |
| brought seed from England to plant apple trees. | produce cider to sell. Farmers returned home and used |
| Later, seedlings and whole trees were transported to | their own method of fermentation to produce cider. |
| the colonies by wealthier colonists who established |  |
| large apple orchards. Although apples were a staple | In 1881, Mr. Ben- |
| in the meager diet of | jamin F. Clyde decided |
| early settlers, the moti- | to produce and sell cider |
| vation for raising apple | in Mystic, now referred |
| trees was equally for | to as Old Mystic. For the |
| the purpose of making | first few years, he |
| cider. Cider was easy | pressed his apples at lo- |
| to make, stored well, | cal mills. Eventually, he |
| and provided a mildly | bought a press and in- |
| alcoholic drink for all to | stalled it in rented space |
| enjoy. Until approxi- | in the corner of a local |
| mately seventy years | saw mill. He received |
| ago, cider was what is | power for his press from |
| now referred to as “hard | the saw mill’s line shaft. |
| cider.” | In 1897, Mr. Clyde de- |
| Cider was an ex- | cided to expand his busi- ness by purchasing his |
| tremely popular bever- | own mill and press. |
| age from the initial |  |
| settlement of the New | Later that year, he |
| World until the early | purchased a No. 2, four |
| twentieth century. | screw press from the |
| Quantities as large as | Boomer and Boschert |
| 10,000 barrels (315,000 gallons) per year for a two | Press Company of Syracuse, New York. From Boomer |
| hundred family community were produced in the early | and Boschert, he also bought the required accesso- |
| eighteenth century [Martin]. Additionally, saloons | ries: an apple grater, an apple elevator and a cider |
| and inns considered cider to be one of their most | pump. As was their practice, Boomer and Boschert |
| popular beverages. The passage of the Volstead Act | also furnished the plans for the building. From his |
| of 1919, more commonly known as Prohibition, re- sulted in the decline of cider’s popularity. | experiences as a teamster, Mr. Clyde decided to use a |
| Apple cider and its production was a significant | 10 H.P. Olney and Warren center crank steam engine and boiler as the power source. Local craftsman constructed the building. Boomer and Boschert sent |
| piece of American culture for several centuries and | technicians to oversee the machinery installation. |
| was the predecessor of today’s massive beverage |  |
| industries. While the processing of apple cider has | The mill has stayed in Mr. Clyde’s family. It is |
| changed over the centuries, B.F. Clyde’s Cider Mill | currently owned and operated by his grandson, Old |
| continues to produce cider as it was produced over a | Mystic native John K. Bucklyn. |
| century ago. From the earliest crude stone-crushed apples to the modern automated hydraulic presses, | Technical Background |
| engineers have devised more efficient means to press apples. The screw press in use at the Mill | The method for making apple cider has changed |
| represents the peak of screw press design used | little over the centuries. The apples including skin, |
| before the hydraulic press became prevalent. | seeds, and core are reduced to pomace (a mix of small |
| History of | pieces of apple) by crushing, cutting, grating or grind- ing. The pomace is pressed to extract the juice which |
| B.F. Clyde’s Cider Mill | is transformed to cider by natural fermentation. In Clyde’s mill, the pomace is laid up in a “cheese” |
| Although cider continued to be produced on | prior to placing under the press for juice extraction. The |
| individual farms for private use, the centrally located | cheese is made using racks, a form, and press cloths. |
| mill became more popular. Because the early mills | Clyde’s rack is a 4' 10" square wood structure consist- |

ing of 72" wide x 3/8" thick slats placed side by side with a 7" gap between them. A second layer of slats 1 3/8" wide x 1/2" thick is placed side by side 1/4" apart on top, per- pendicular to the first layer. These two layers are tacked together at each intersection to form the rack. The form is a square wood frame about 3 1/2" deep, but with inside dimensions slightly smaller than the rack. The form is placed on top of the rack. A 96" square press cloth is placed in the form with a corner over- lapping each side. Pomace drops down from the chute into the press cloth lined rack and form. Once the form is filled, the cloth is folded over the pomace. The form is removed and the process is repeated with an- other rack, form and press cloth until the desired number of layers is reached. The series of racks and pomace in the press cloths form the

cheese.

The mechanical engineering aspect of cider mak- ing is found in the evolution of the machinery used to perform the required tasks. One of the earliest meth- ods required the individual to place apples in a circular trough and roll heavy stones over them. The early cider presses were constructed by the farmer. A large wooden screw was attached to the frame at the top. An opening was made at the bottom so a pole could be used to help turn the screw [Orton].

In the latter half of the 19th century, presses were manufactured and sold to farmers for cider and wine making. The early presses were of the screw type. Later, hydraulic presses became more common. Manufacturers also made devices to crush and grind the apples into pomace.

In 1874, Boomer and Boschert Company was founded to produce presses and their accessories for wine and cider making. Their first press was a knuckle joint press, which is similar in operation to a modern day automobile scissors jack. Later, they developed screw presses and hydraulic presses. The accessory equipment included the apple elevator, the apple grater, and the juice pump. In 1897, the company also introduced the Becker pomace chute. This unique, telescoping chute allowed the cider maker to drop the pomace a few inches above each layer, greatly reduc- ing the spillage common to a conventional fixed height pomace chute. Today, Clyde’s Cider Mill continues to utilize the No. 2 screw press and the aforementioned accessories.

The mill featured a sophisti- cated method of grinding the fruit and a press capable of applying pressure at three speeds. This model, using all steel construction, was considered the finest screw ci- der press ever made. In the twenti- eth century, the hydraulic press came into widespread use. Thus, B.F. Clyde’s Cider Mill is represen- tative of the final and finest mills using the mechanical screw press.

Mechanical Specifïcations

The mill machinery is powered off the single line shaft with appropri- ately sized pulleys and belts except for the apple elevator which is driven by a specially geared right angle drive off of the line shaft.

The main elements are:

Steam Engine - Ames 15 Horsepower with a Gardener governor. Manufactured circa 1895-1900. Drives line shaft at 250 RPM.

Cider Press - Boomer & Boschert No. 2; four 2 1/2" X 3 threads per inch power screws capable of being driven at three different speeds; 4'10" square racks with 96" square press cloths; maximum stroke of 48". Maximum capacity is approximately 10,000 pounds per day (1100 gallons). Manufactured in the mid 1890's.

Steam Boiler - Dutton 15 Horsepower fire tube

with a riveted shell. Manufactured in 1942.

Features  of  the  No.  2  Screw  Press

The No. 2 screw press by Boomer and Boschert

Apple Grater - Boomer & Boschert; 10 knives

has a number of innovative features which have ex- tended its usefulness to nearly one hundred years after

on 1 7/16" shaft rotating at 2000 RPM. Manufactured in the mid 1890's.

Cider Pump - Boomer & Boschert; bronze plunger pump, 3" cylinder with 4 1/2" stroke. Runs at not greater than 80 strokes per minute; a capacity of 10 gallons per minute. Manufactured in the mid 1890's.

Apple Elevator - Boomer & Boschert; lifts apples from storage up to grater. Lifts up to 20 bushels per minute. Manufactured in the mid-1890's.

it was installed. These features include: an invention to

reduce friction between the screws and washers, a

mechanical “strain gage”, and a three speed drive.

The screw is attached to the overhead frame by means of a spur gear nut and washer. The frame bends when cider is being pressed from the apples causing the nut to bend and bind on the screw. To eliminate this problem, Boomer and Boschert invented a mechanism which allows the nut to bend with the head beams. The Boomer and Boschert catalog de- scribes the invention as follows:

The spur gear nut A is separated from the washer B by the self-adjusting concave washer D. The convex portion of B is the exact segment of a globe, and D turns with the nut or remains stationary, the nut turn- ing on top of it. It is made with sufficient play to allow

it to conform to any spring or warp of the head beams and still main- tain the nut A in its proper position, ren- dering it im- possible to bind or cramp on the screw.

The indicator or “strain gage” consists of a slen-

The press is started and cider is squeezed from the cheese. The cider is channelled into a hole in the

der pointer attached to the upper steel press beam. The indicator is attached at one end by means of a screw and supported in the middle by a bolt. Above the attached end is a scale which indicates the relative amount of load being applied to the beam. Since the press is manually operated, the operator can quickly determine how much pressure is being applied by the press.

A three speed drive has been incorporated in the design of the press to insure that as much juice as possible is squeezed from the apples. According to their catalog, “This (the three speed drive) enables the operator to run down until the head strikes the cheese; then shift to the medium motion, until the bulk of the cider is extracted, and to finish on the slow speed, the power [force] increasing as the speed decreases.”

Operation of the Press

The process begins by

placing the apples in the storage structure. From storage, apples are washed and transported up to the second story of the mill building where they are dropped into the grater. The grater turns apples into pomace which falls through the telescoping chute to the first layer of the cheese on the press table. After the cheese has been prepared, the table is ro- tated 180 degrees to place the end with the cheese under the press. Each end of the table is capable of carrying a cheese. Thus, while the first cheese is being pressed, another cheese can be laid up. This feature mini- mizes the down time of the press.

press table and then into the press hold tank. From the press hold tank, it is pumped into the main hold tank where it is dispensed into the cider containers.

References

les.

tory Martin, Alice A. All About App Houghton Mifflin

k - The S Company: Boston, 1976. Cider Boo

Orton, Vrest. The American verage.

tural Be No. 54. Farrar, Straus and

rica’s Na	Catalogue

Giroux: New York, 1973. of Ame

hiner - nd Mac

Cider a	The

Dunning & Boschert Press: Syracuse, New York, 1954.

Acknowledgements

Many thanks to Al Duncan, the History and Heritage chairman of the New London Section for coordinating all details concerning the dedication of B.F. Clyde’s Cider Mill as a landmark.

Special thanks to Glenn Melnyk for all the photo- graphs published in this brochure.

Thanks to Greg and Jenni Yow for their assis- tance in the publication of this brochure.

The History and Heritage Program of ASME

designated. Since the ASME History and Heritage

Program began, 165 Historic Mechanical Engineering Landmarks, 6 Mechanical Engineering Heritage Sites, and 6 Mechanical Engineering Heritage Collections

The ASME History and Heritage Recognition

have been recognized. Each reflects its influence on society, either in its immediate locale, nationwide, or

Program began in September 1971. To implement

and achieve its goals, ASME formed a History and

throughout the world.

Heritage Committee, composed of mechanical engi- neers, historians of technology, and the Curator Emeritus of Mechanical and Civil Engineering at the Smithsonian Institution. The Committee provides a public service by examining, noting, recording, and acknowledging mechanical engineering achieve- ments of particular significance. The History and Heritage Committee is part of the ASME Council on Public Affairs and Board on Public Information. For further information, please contact Public Information, The American Society of Mechanical Engineers, 345 East 47 Street, New York, NY 10017-2392, 212-705-7740; telefax 212-705-7141.

The B. F. Clyde Cider Mill is the 112th National Historic Mechanical Engineering Landmark to be

An ASME landmark represents a progressive step in the evolution of mechanical engineering. Site designations note an event or development of clear historical importance to mechanical engineers. Collec- tions mark the contributions or a number of objects with special significance to the historical development of mechanical engineering.

The ASME Historic Mechanical Engineering Rec- ognition Program illuminates our technological Heritage and serves to encourage the preservation of the physi- cal remains of historically important works. It provides an annotated roster for engineers, students, educators, historians, and travelers, and helps establish persistent reminders of where we have been and where we are going along the divergent paths of discovery.

Large spur gear on screws.

Right hand thread screw nut

Left hand thread screw nut.

Head socket washer.

Cover for same

Spur pinion sliding on upright.

Yoke.

Split collar on pinion.

Brass washer between split collar and yolk.

Large bevel gear.

Bearing for same

Bevel pinion.

Shaft boxes.

Cap for same.

Large spur driving gear.

Pinion to match.

Medium spur gear, upper shaft.

Pinion to match, lower shaft.

Large center spur gear.

Long center pinion.

Top casting on screws.

Lever quadrant.

Double lever quadrant.

Lower screw washer.

Pulley, fast to shaft.

Pulley fast to long center pinion.

Pulley loose on shaft.

Bronze plano concave washer under nut.

Fork for shifting lower shaft.

Yoke box.

Screw -  right hand thread.

Screw left hand thread.

Upper shaft.

Lower shaft.

Upright end shaft.

Rod for shifting lower shaft.

Collar on end shafts.

37½. Finger for shifter.

Loop for shifter.

Bracket for self-shifter.

Bell crank for self-shifter.

Shifter bar bracket.

The  American  Society  of  Mechanical  Engineers

| President | Paul J. Torpey |
| --- | --- |
| Vice President, Region I | Robert G. Jeffers, Ph.D., P.E. |
| History and Heritage Chairman, Region I | Fred E. Angilly, P.E. |
| Senior Vice President, Public Affairs | John R. Parker, P.E. |
| Vice President, Public Information | Erwin Fried, P.E. |
| Executive Director | Dave Belden, Ph.D, P.E. |
| Director, Northeast Regional Office | James J. Reffelt |
| ASME New London Section Chairman | Jayne F. Scott |
| Vice Chairman | Vince Wilczynski |
| Secretary | Sandor Becz |
| Treasurer | George Ziegra |
| History and Heritage Chairman | Alex Duncan |

The  ASME  National  History  and  Heritage  Committee

| Chairman | James L. Lee, P.E. |
| --- | --- |
| Secretary | Robert M. Vogel |
| Staff Liaison | Diane Kaylor |
| Regional Publicity | Tom L. McDonough, P.E. |
| B.F. Clyde’s Cider Mill Owner | John Bucklyn |

NATIONAL  HISTORIC

MECHANICAL  ENGINEERING  LANDMARK B.F.  CLYDE’S  CIDER  MILL

1898

CLYDE’S MILL IS A RARE SURVIVOR OF A ONCE-COMMONPLACE SEASONAL RURAL INDUSTRY. UNTIL WELL INTO THIS CENTURY A CIDER MILL COULD BE FOUND IN EVERY COMMUNITY WHERE APPLES WERE GROWN, IN THE FALL CONVERTING THE FRUIT OF THE ORCHARD INTO DRINK EVEN AS THE GRIST MILL CONVERTED THE GRAIN OF THE FIELD INTO FLOUR.

THE MACHINERY AT CLYDE’S - FOR ELEVATING THE APPLES TO THE GRINDER, FOR GRINDING THE APPLES INTO PULP, AND FOR PRESSING THE PULP INTO CIDER - WAS MANUFACTURED BY PRESS-BUILDER BOOMER & BOSCHERT OF SYRACUSE, NEW YORK ALSO DESIGNER OF THE BUILDING.

The American Society of

Mechanical Engineers

1994 NL112.