# 2019 MMOGTA 8 MPH Class Rules/Division 4

## Classes: 4000, 4500, 5000, 5500

- Drivers must be at least 16 years old and operate in a safe manner, speed not to exceed 4 mph off the track. Contestants less than 18 years old must have written permission from parent or guardian and they must be at trackside at time of pull.

- Any agricultural updraft carburetor allowed. Number of barrels, throats, and venturi must be same as the stock carburetor for the make and model of tractor (JD can use Duplex carb).

- Tractors must run stock RPM’s (no load M&W RPM chart).  20% margin of error allowed.

- Tractors may pull in any gear. Torque Amplifiers may be used.

- Max tire in all classes is 18.4-38.

- Tires may be cut in any way. Any rim width may be used.

- Hitch no higher than 20 inches and no closer than 18 inches from center or rear axle to hitching point.  Hitch/drawbar must be rigid in all direction. Hitch material must be a minimum of ¾ inch thick and have 3/4-inch material around the hole. Opening for hook must be at least 3.5 inches in diameter or a 3-inch x 3.5-inch hole may be used (hook must swing freely). No twisted or vertical clevises If turnbuckles are used they must be category one and use a ¾ inch bolt for mounting.

- Wheelie bars are mandatory. They must be independent of hitch, must be at least 4” behind the tires, no higher than 10 inches off the ground, no closer than 20 inches together, must have 5” x 5” or larger pads and must support the weight of the tractor in its heaviest class.

- All tractors must have a working breakaway kill switch and fenders.

- There will be a 125 foot speed limit cone.

- All rules, unforeseen problems or oversights will be ruled on by the tech committee and the chairman of the class, with their decision being final. Rules frozen for the 2020 season with exception to safety, oversights and unforeseen concerns.

For further information contact:

Cory Urbain 989-529-5429